## Slide 1: Electron Microscope

## Slide 2: Light vs EM
Which is which? What are the main differences?

## Slide 3: SEM vs TEM
A seed viewed with a scanning EM

## Slide 4: Learning Objectives
Know the difference between a transmission and a scanning electron microscope
Explain the benefits of electron microscopes
Compare and contrast EM & LM

## Slide 5: Electron Microscope
EM generates beam of electrons
Electron beam passes through very thin prepared sample
Resolution is 0.5nm

## Slide 6: Preparing Slide of EM
Fix specimen in gluteraldehyde
Dehydrate with ethanol
Embed in resin
Slice thinly
Stain (salts of heavy metals – eg lead, uranium)
Mount on copper grid
Place in vacuum (allows electrons to travel towards specimen)

## Slide 7: Transmission Electron Microscope
Electrons pass through denser part of sample less easily so create contrast
2D
Magnification up to x250 000

## Slide 8: Scanning Electron Microscope
Electrons ‘bounce’ off metal-salt-stained sample
3D
Magnification x100 000

## Slide 9
Electron Microscopes | Light Microscopes
Maximum resolution is 0.5nm | Maximum resolution is 200nm
Useful magnification is up to 250,000x in TEM, 100,000x in SEM | Useful magnification is around 1000x (1500x at best)
Wavelength is 1.0nm. | Wavelength is between 400-700nm.
Highly detailed images, and even 3D surface imaging. | See reasonable detail, with true colours.
Can see organelles of cells, bacteria and even viruses. | Good for small organisms, invertebrates and whole cells.
Comparision of EM and LM

## Slide 10: Advantages/Disadvantages of EM
Advantages of EM | Disadvantages of EM
Resolution is x2000 more than LM | Samples have to be placed in a vacuum
Produces detailed images | Very expensive
SEM produces 3D images | Need to be highly skilled to create samples